The default baud rate appears to be 115200 with No parity, 8 data bits, 1 stop bit so set your terminal emulator with those settings for the connection. I use Xon/Xoff handshaking but I'm unsure if it matters at that baud rate

MEMORY MAP

BASE	TOP	DESCRIPTION	NOTES
0x1000_0000	0x1000_FFFF	UART 0
0x1001_0000	0x1001_FFFF	UART 1
0x1002_0000	0x1001_FFFF	UART 2

https://linux-sunxi.org/images/d/d2/Dw_apb_uart_db.pdf

UART MEMORY MAP

OFFSET	NAME	DESCRIPTION
0x00	rx	Register to transmit data
0x00	tx	Register to receive data
0x7c	usr	UART status register

Context switching
https://github.com/torvalds/linux/blob/master/arch/riscv/kernel/entry.S

Entry point
https://github.com/torvalds/linux/blob/master/arch/riscv/kernel/head.S